## Slide 1: Lab4 Model Compression：Pruning & Quantization

## Slide 2: Concept (pruning)
Network pruning is widely used for reducing the heavy inference cost of deep models in low-resource settings. A typical pruning algorithm is a three-stage
pipeline.
Training
Pruning
Fine-tuning
repeat

## Slide 3: Why pruning?
According to “Lottery Ticket Hypothesis” (Frankle & Carbin, 2019), we find that large network is easier to train than small network.
easy to train
hard to train

## Slide 4: Method (pruning)
Pruning the channel of each convolution layer based on the weight of batch normalization.
BN：
The smaller the value of γ , the less important of .

## Slide 5: DATASET
Speech Commands
TensorFlow released the Speech Commands Datasets. It includes 65,000 one-second long utterances of 30 short words, by thousands of different people.
We only use 10 short words.

## Slide 6: Network
SincNet
SincNet is a neural architecture for processing raw audio samples.
It is a novel Convolutional Neural Network (CNN) that encourages the first convolutional layer to discover more meaningful filters.

## Slide 7: Task 1 (sincnet_training.ipynb)
Train SincNet
  Determine super parameter.
  Let the best validation accuracy be larger than 80%.

## Slide 8: Task 2 (sincnet_pruning.ipynb)
Prune SincNet
  Determine the pruning rate (percentage of total channel will be pruned).
  Observe channel amount and accuracy before and after pruning.
Don’t set too large at the first iteration.
After pruning

## Slide 9: Task 2 (sincnet_pruning.ipynb)
Prune SincNet
  Observe parameter of network and accuracy before and after pruning.
  Prune the model that have been fine-tuned repeatedly for twice.
Before pruning
After pruning
?
Fine-tuning
?

## Slide 10: Concept (quantization)
Quantization stores tensors at lower bit-widths than floating point. This allows for a more compact model representation and the use of high performance vectorized operations on many hardware platforms.

## Slide 11: Method (quantization)
Change the range and precision of initial weight.
0.73
Ex: number_of_bits = 8
Range: 0~1
FP32
187
Range: 0~255
INT
weight

## Slide 12: Task 3 (sincnet_quat.ipynb)
Train SincNet_Quat
  Determine super parameter.
  Let the best validation accuracy be larger than 70%.
  Observe the training process between with and without quantization.

## Slide 13: Task 4 (Report)
Report should include
  The screenshot of training result from task 1 (score：10%)
  The screenshot of training result from task 2 (score：10%)
  Explain Pruning briefly (What/Why/How) (score：20%)
  The screenshot of training result from task 3 (score：10%)
  Explain Quantization briefly (What/Why/How) (score：20%)
  Compare the difference from above methods of compression (score：30%)
Submit deadline：1 week only (2024/11/11, 23:59)
You only need to submit your report file
Please strictly follow the naming rule !!!!!
學號_lab4_report.pdf

## Slide 14: Reference
PRUNING TUTORIAL
  https://pytorch.org/tutorials/intermediate/pruning_tutorial.html
Rethinking the Value of Network Pruning
  https://github.com/Eric-mingjie/rethinking-network-pruning
SincNet
  https://github .com/mravanelli/SincNet
Post-training Static Quantization — Pytorch
  https://medium.com/@sanjanasrinivas73/post-training-static-quantization-pytorch-37dd187ba105
Speech commands
  https://arxiv.org/abs/1804.03209

## Slide 15: Shut down your kernel !!!!!
Remember to SHUTDOWN the kernel to release resources for others